## Slide 1: Research Plan
Carrier Board Design
  Circuit boards made to power and access the MCUs under test
Testing Conditions
Treatment Details
Testing Location
Device Selection
  Criteria for selecting which microcontrollers would be tested
Procedure

## Slide 2: Carrier Boards
The first step of the research program
Provide regulated power and other necessary support to the chips
Custom board for each MCU model
Onboard power regulator
Transformer, rectifier, filter capacitor located outside the test chamber
Sensor to measure MCU temperature
Connector for clock out, temperature, power and ground
MCU soldered directly to board in surface-mount package (no socket)
Board made as small as practical

## Slide 3: Testing Conditions
RF energy applied to top of chip package
No heatsinks or other covering will be applied to the MCU
5 devices will be tested at a time
No two MCUs of the same model will be placed into the same trial
Analysis will look for variation from trial to trial, to discover outside contamination
Analysis will look for variation from trial to trial, to discover outside contamination
Within a treatment, each set will be selected at random

## Slide 4: Testing Conditions, Continued
MCU’s fastest internally-generated clockrate, without PLL, will be used
Half-wave dipole antennas used to transmit RF, 1MHz antenna is inductively loaded
2 test stands, each holding 5 boards, 3D printed. One used while the other is prepared.
Antenna placed in center of stand
Experimental and control trials will be interleaved

## Slide 5: Treatment Details
2 factor experiment: frequency and power density, 28 treatments total
Dependent variable: clock drift of an MCU's internal oscillator
7 frequencies
4 power density levels, based on effective useful range of transmission
3 MCUs of each model * 7 frequencies * 4 power densities * 20 MCU models / 5 MCUs per trial = 336 trials
60 control MCUs / 5 MCUs per trial = 12 control trials

## Slide 6: Treatment Details, Continued
  1 MHz – AM broadcast
  100 MHz – FM broadcast
  600 MHz – UHF TV broadcast
  850 MHz – common long-range cellular band
  1900 MHz – common short-range, high-density cellular band
  2400 MHz – WiFi B/G/N
  5500 MHz – WiFi A/N/AC

## Slide 7: Testing Location
Testing to be performed at commercial RF test facility
Temperature must be controlled within ± 1º Celsius
Temperature measured to ±0.1ºC for correction of thermal clock drift
Temperature logged during tests
RF measured during control trials

## Slide 8: Device Selection
MCUs selected from 4 major microcontroller vendors
  NXP Semiconductor
  ST Microelectronics
  Texas Instruments
  Microchip Technology
Individual models chosen based on their feature sets
Newer parts preferred, to make project relevant for as long as possible
Oscillator design often shared among similar models, diversity was preferred

## Slide 9: Procedure
MCUs placed onto test stand, cable connected
Chamber closed and RF generator turned on
  Allowed stabilize for 5 minutes before measurement
Measurement of clockrate and temperature begins
  Temperature used to correct for thermal clock drift
Measurement continues for 1 hour
  Frequency measured every minute
  First available data graphed to check for unexpected behavior
Total number of cycles recorded after trial
  Overall drift calculated from this
All measurements retained for analysis and quality control